## Slide 1: Current System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
¾” Garden Hose
Notes
Maximum pressure is 4 psi before pipe losses
Flow rate was measured at 2.2 GPM
Water does not flow from tank to garden effectively
3.03 PSI
2.2 GPM, ~0 psi

## Slide 2: Modified System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Minimal Cost
Increase in pressure
Can not use garden hose or sprinklers
Can fill can in 6 seconds (hypothetically)
3.03 PSI
20+ GPM, ~4 psi

## Slide 3: Gravity System
7 ft
Garden (assume flat plane)
14 ft
Height between tank and garden
Height of tank
¾” Garden Hose
Notes
Increases pressure to about 10 psi
Might make a garden hose usable, not sprinklers
Might be less safe, requires raising tank
3.03 PSI
2” Pipe
9.5 PSI

## Slide 4: Manual Pump System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
More complex + $
Limited flow rate OR pressure (tradeoff)
Requires constant pumping
Most likely would need 2 people (1-pump, 1-water)
3.03 PSI
psi/gpm per pump spec
Pump Apparatus
Human Energy

## Slide 5: Pump System with tank
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
More complex + $$
Requires pumping to maintain pressure
Flowrate/pressure determined by tank height
Pumping time is affected by tank size
3.03 PSI
psi/gpm per tank height
Pump Apparatus
Human Energy
Raised Tank

## Slide 6: Pump System with pressure tank
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
More complex + $$
Requires pumping to maintain pressure
Pumping time is affected by tank size
Can be harder to implement
Requires higher pressure to hold more water
3.03 PSI
psi/gpm as design specs
Pump Apparatus
Human Energy
Pressure Tank

## Slide 7: Solar Pump System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
More complex + $$
Would have limited flowrate/pressure
Need large solar panel
Be operational only during daylight
3.03 PSI
psi/gpm per pump spec
Pump Apparatus
Solar Energy

## Slide 8: Solar + Pressure
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have better flowrate/pressure
Would have spotty service
3.03 PSI
Pump Apparatus
Solar Energy
psi/gpm as design specs
Pressure Tank

## Slide 9: Solar + Raised
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have good flowrate/pressure
Not very sustainable
May be unsafe
Might be unsightly
3.03 PSI
psi/gpm per tank height
Raised Tank
Pump Apparatus
Solar Energy

## Slide 10: Battery Pump System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
More complex + $$
Would be less limited energy
Would require charging
More expensive
3.03 PSI
psi/gpm per pump spec
Pump Apparatus
Battery Energy

## Slide 11: Battery + Pressure
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have better flowrate/pressure
Would have spotty service
3.03 PSI
Pump Apparatus
Battery Energy
psi/gpm as design specs
Pressure Tank

## Slide 12: Battery + Raised
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have good flowrate/pressure
Not very sustainable
May be unsafe
Might be unsightly
3.03 PSI
psi/gpm per tank height
Raised Tank
Pump Apparatus
Battery Energy

## Slide 13: Grid Pump System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
More complex + $
Would have best flowrate/pressure
Cheaper than battery/solar
Not very sustainable
3.03 PSI
psi/gpm per pump spec
Pump Apparatus
Grid Energy

## Slide 14: Grid + Pressure
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have best flowrate/pressure
Not very sustainable
3.03 PSI
Pump Apparatus
Grid Energy
psi/gpm as design specs
Pressure Tank

## Slide 15: Grid + Raised
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have good flowrate/pressure
Not very sustainable
May be unsafe
Might be unsightly
3.03 PSI
psi/gpm per tank height
Raised Tank
Pump Apparatus
Grid Energy

## Slide 16: Modified System
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Minimal Cost
Increase in pressure
Can not use garden hose or sprinklers
Can fill can in 6 seconds (hypothetically)
3.03 PSI
20+ GPM, ~4 psi

## Slide 17: Solar + Pressure
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have better flowrate/pressure
Would have spotty service
3.03 PSI
Pump Apparatus
Solar Energy
psi/gpm as design specs
Pressure Tank
20+ GPM, ~4 psi

## Slide 18: Solar + Raised
7 ft
Garden (assume flat plane)
4 ft
Height between tank and garden
Height of tank
2” Pipe
Notes
Complex + $$$
Would have good flowrate/pressure
Not very sustainable
May be unsafe
Might be unsightly
3.03 PSI
psi/gpm per tank height
Raised Tank
Pump Apparatus
Solar Energy
20+ GPM, ~4 psi