## Slide 1: EMCH 368 Lab 10
Exercise #2 Directions
-Jacob Vaught, Spring 2024

## Slide 2
Open Matlab
Start SimuLink

## Slide 3
Create a new model once the simulink window appears.
This process can take upwards of 10 minutes depending on your machine.

## Slide 4
Open the Library Browser once the Blank Model is loaded.

## Slide 5
Our first component is the 'Continuous Pulse Generator’
To place on the screen, click, hold, and drag into the desired location

## Slide 6
Our first component is the 'Continuous Pulse Generator’
Set the amplitude to 100
Set the period to 10 secs
Set the Puse Width to 50%

## Slide 7
Our next component is the Transfer Function.
To modify values of the component, we double-click, OR right-click and select parameters
Set Numerator to [1]
Set Denominator to [0.1 1]

## Slide 8
We click, drag and hold to create a connection between blocks

## Slide 9
Add a sum to the model.
Set the List of Signs in the parameters to |+-

## Slide 10
Now we want to add 3 product blocks for each of the PID controller components.

## Slide 11
Now we will want to add some constants for the PID Controller.
Note that holindg the spacebar for a second will auto-scale the screen to your model.
Space + left-mouse is to move the screen around

## Slide 12
We will add the integrator for the Integral component of the PID controller.

## Slide 13
We will add the Derivator for the derivative component of the PID controller.

## Slide 14
Change the switch value to a 1 for linearization.

## Slide 15
Add a summing component, and set the List of Signs to +++

## Slide 16
Add the system Transfer Function
Set Numerator to [1 10]
Set Denominator to [1 1 10]

## Slide 17
Add 2 step functions to represent the maximum and minimum error.
Connect the original sum to the output of the transfer function.
Set the Step Time to 0 for both.
Set the Final Value to 90 for one and 110 for the other.

## Slide 18
Set the Step Time to 0 for both.
Set the Final Value to 90 for one and 110 for the other.

## Slide 19
Add 2 step functions to represent the maximum and minimum error.
Connect the original sum to the output of the transfer function.
Set the Step Time to 0 for both.
Set the Final Value to 90 for one and 110 for the other.

## Slide 20
Add a scope to view the outputs of the system. It should connect to
  2 step blocks
  Output of the system
  And the reference
To tune the system, adjust the block parameters of each of the constants.

## Slide 21
Double-click on the scope, and press the run button.
The graph should appear.

## Slide 22
We want a dashed line for the 90% and 110%.
Select the Properties for the step blocks
Then change the line-type to dashed
Then change the width to 2.0